## Slide 1
Chapter 3
Data and Signals
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2: Data and Signals
Data are entities that convey meaning (computer file, music on CD, results from a blood gas analysis machine)
Signals are the electric or electromagnetic encoding of data (telephone conversation, web page download)
Computer networks and data/voice communication systems transmit signals
Data and signals can be analog or digital – this can be misleading – let’s talk more about this
TDC 361

## Slide 3: Analog vs. Digital Signals
Signals can be interpreted as either analog or digital
In reality, all signals are analog
Analog signals are continuous, non-discrete
Digital signals are non-continuous, discrete
Digital signals lend themselves more nicely to noise reduction techniques

## Slide 4: Analog vs. Digital Signals
There are actually multiple “kinds” of digital signals
Discrete square waveforms found in digital systems such as LANs (see an example on the next slide)
Digital logic voltage levels (a binary 0 is 0 to 2 volts; a binary 1 is 4 to 6 volts)
Analog signals which can only be interpreted in a finite number of ways (modulation techniques such as QAM-16)

## Slide 5
Figure 3.1 Comparison of analog and digital signals

## Slide 6: Time domain concepts
Continuous signal
  Infinite number of points at any given time
Discrete signal
  Finite number of points at any given time; maintains a constant level then changes to another constant level. So time is discrete but amplitude is continuous.
Periodic signal
  Pattern repeated over time
Aperiodic (non-periodic) signal
  Pattern not repeated over time

## Slide 7: Time domain concepts
In data communications, we commonly use periodic analog signals and nonperiodic digital signals.
Periodic analog signals can be classified as simple or composite.
A simple periodic analog signal, a sine wave, cannot be decomposed into simpler signals.
A composite periodic analog signal is composed of multiple sine waves.

## Slide 8
Figure 3.2 A sine wave

## Slide 9: Signal Properties
All signals are composed of three properties:
  Amplitude
  Frequency
  Phase

## Slide 10
Figure 3.3 Two signals with the same phase and frequency, but different amplitudes

## Slide 11
Frequency and period are the inverse of each other.
Note

## Slide 12
Figure 3.4 Two signals with the same amplitude and phase, but different frequencies

## Slide 13
Table 3.1 Units of period and frequency

## Slide 14
The power we use at home has a frequency of 60 Hz. The period of this sine wave can be determined as follows:
Example 3.3

## Slide 15
The period of a signal is 100 ms. What is its frequency in kilohertz?
Example 3.5
Solution
First we change 100 ms to seconds, and then we calculate the frequency from the period (1 Hz = 10−3 kHz).

## Slide 16
Frequency is the rate of change with respect to time. Change in a short span of time
means high frequency. Change over a long span of time means low frequency.
Note

## Slide 17
If a signal does not change at all, its frequency is zero.
If a signal changes instantaneously, its frequency is infinite.
Note

## Slide 18
Phase describes the position of the waveform relative to time 0.
Note

## Slide 19
Figure 3.5 Three sine waves with the same amplitude and frequency, but different phases

## Slide 20
A sine wave is offset 1/6 cycle with respect to time 0. What is its phase in degrees and radians?
Example 3.6
Solution
We know that 1 complete cycle is 360°. Therefore, 1/6 cycle is

## Slide 21
Figure 3.7 The time-domain and frequency-domain plots of a sine wave

## Slide 22
The frequency domain is more compact and useful when we are dealing with more than one sine wave. For example, Figure 3.8 shows three sine waves, each with different amplitude and frequency. All can be represented by three spikes in the frequency domain.
Example 3.7

## Slide 23
Figure 3.8 The time domain and frequency domain of three sine waves

## Slide 24
Figure 3.10 Decomposition of a composite periodic signal in the time and frequency domains

## Slide 25
A single-frequency sine wave is not useful in data communications;
we need to send a composite signal, a signal made of many simple sine waves.
Note

## Slide 26
Figure 3.11 The time and frequency domains of a nonperiodic signal, such
someone speaking into a microphone

## Slide 27
The bandwidth of a composite signal is the difference between the
highest and the lowest frequencies contained in that signal.
Note

## Slide 28
Figure 3.12 The bandwidth of periodic and nonperiodic composite signals
Note: each
frequency is
identifiable
Note:
frequencies
are all over
the place

## Slide 29
If a periodic signal is decomposed into five sine waves with frequencies of 100, 300, 500, 700, and 900 Hz, what is its bandwidth? Draw the spectrum (range of frequencies), assuming all components have a maximum amplitude of 10 V.
Example 3.10

## Slide 30
Solution
Let fh be the highest frequency, fl the lowest frequency, and B the bandwidth. Then
Example 3.10 (continued)
The spectrum has only five spikes, at 100, 300, 500, 700, and 900 Hz (see Figure 3.13).

## Slide 31
Figure 3.13 The bandwidth for Example 3.10

## Slide 32
A nonperiodic composite signal has a bandwidth of 200 kHz, with a middle frequency of 140 kHz and peak amplitude of 20 V. The two extreme frequencies have an amplitude of 0. Draw the frequency domain of the signal.
Solution
The lowest frequency must be at 40 kHz and the highest at 240 kHz. Figure 3.15 shows the frequency domain and the bandwidth.
Example 3.12

## Slide 33
Figure 3.15 The bandwidth for Example 3.12

## Slide 34
3-3 DIGITAL SIGNALS
In addition to being represented by an analog signal, information can also be represented by a digital signal. For example, a 1 can be encoded as a positive voltage and a 0 as zero voltage. A digital signal can have more than two levels. In this case, we can send more than 1 bit for each level.
Bit Rate Bit Length Digital Signal as a Composite Analog Signal
Application Layer
Topics discussed in this section:

## Slide 35
Figure 3.16 Two digital signals: one with two signal levels and the other with four signal levels

## Slide 36
A digital signal has eight levels. How many bits are needed per level? We calculate the number of bits from the formula
Example 3.16
Each signal level is represented by 3 bits.

## Slide 37
What about a digital signal with 16 levels?
How many bits are needed per level?
What about 32 levels? 64 levels? 128 levels?
What about 9 levels??
2? = 9?
3.17 bits
However, this answer is not realistic.
Example 3.17

## Slide 38
Assume we need to download text documents at the rate of 100 pages per second. What is the required bit rate of the channel?
Solution
A page is an average of 24 lines with 80 characters in each line. If we assume that one character requires 8 bits, the bit rate is
Example 3.18

## Slide 39
A digitized voice channel, as we will see in Chapter 4, is made by digitizing a 4-kHz bandwidth analog voice signal. We need to sample the signal at twice the highest frequency (two samples per hertz). We assume that each sample requires 8 bits. What is the required bit rate?
Solution
The bit rate can be calculated as
Example 3.19

## Slide 40
What is the bit rate for high-definition TV (HDTV)?
Solution
HDTV uses digital signals to broadcast high quality video signals. The HDTV screen is normally a ratio of 16 : 9. There are 1920 by 1080 pixels per screen, and the screen is renewed 30 times per second. Twenty-four bits represents one color pixel.
Example 3.20
The TV stations reduce this rate to 20 to 40 Mbps through compression.

## Slide 41
Figure 3.18 Baseband transmission
Digital transmission on a wire typically “consumes” the entire channel
and is labeled baseband signaling.
A digital signal is a composite analog signal with infinite bandwidth.
The LAN is a common example of baseband signaling.

## Slide 42
Figure 3.20 Baseband transmission using a dedicated medium
This is ideal.
This is what we get.
Still readable however.

## Slide 43: Fourier Analysis
Interestingly, digital signals are combinations of analog signals
Fourier Analysis – any composite signal is a combination of simple sine waves with different frequencies and amplitudes
These simple sine waves are also called harmonics

## Slide 44: Fourier Analysis
Square wave: (4A/ Pi)sin(2 Pi ft) + (4A/3 Pi)sin(2 Pi 3ft) + (4A/5 Pi)sin(2 Pi 5ft)…
Sawtooth: (2A/ Pi ) x [sin(2 Pi ft) – (1/2)sin(2 Pi 2ft) + (1/3)sin(2 Pi 3ft) – (1/4)sin(2 Pi 4ft) …
www.falstad.com/fourier

## Slide 45
Note
In baseband transmission, the required bandwidth is proportional to the bit rate;
if we need to send bits faster, we need more bandwidth.

## Slide 46
Table 3.2 Bandwidth requirements
Bandwidth (B) = 3N/2
where N= Bit Rate
Bandwidth (B) = 5N/2
where N= Bit Rate

## Slide 47
What is the required bandwidth of a low-pass channel if we need to send 1 Mbps by using baseband transmission?
Solution
The answer depends on the accuracy desired.
a. The minimum bandwidth, is B = bit rate /2, or 500 kHz.
b. A better solution is to use the first and the third harmonics with B = 3 × 500 kHz = 1.5 MHz.
c. Still a better solution is to use the first, third, and fifth harmonics with B = 5 × 500 kHz = 2.5 MHz.
Example 3.22

## Slide 48
We have a low-pass channel with bandwidth 100 kHz. What is the maximum bit rate of this channel?
Solution
The maximum bit rate can be achieved if we use the first harmonic. The bit rate is 2 times the available bandwidth, or 200 kbps.
Example 3.22

## Slide 49
Figure 3.23 Bandwidth of a bandpass channel

## Slide 50
If the available channel is a bandpass channel, we cannot send the digital signal directly to the channel; we need to convert the digital signal to an analog signal before transmission.
Note

## Slide 51
Figure 3.24 Modulation of a digital signal for transmission on a bandpass channel

## Slide 52
3-4 TRANSMISSION IMPAIRMENT
Signals travel through transmission media, which are not perfect. The imperfection causes signal impairment. This means that the signal at the beginning of the medium is not the same as the signal at the end of the medium. What is sent is not what is received. Three causes of impairment are attenuation, distortion, and noise.
Attenuation Distortion Noise
Topics discussed in this section:

## Slide 53
Figure 3.26 Attenuation (the first impairment)
Attenuation means a loss of energy.
When a signal, simple or composite, travels through a medium, it loses some of its energy in overcoming the resistance of the medium. To compensate for this loss, amplifiers are used to amplify the signal.

## Slide 54: Decibels
Signal strength is measured in decibels (dB)
dB is a relative measure of loss (or gain). Decibel measures the relative strengths of two signals or one signal at two different points.
NdB = 10 x log10 (P2 / P1)
  P2 = ending power level in watts
  P1 = beginning power level in watts
Example: P1 = 10 watts, P2 = 5 watts
Even easier – remember ½ rule
Losses and gains are additive
Note that-”The decibel is negative if a signal is attenuated and positive if a signal is amplified.”

## Slide 55
Example 3.26
As the result shows –ve sign, so attenuation (loss) of power = 3dB.
A loss of 3dB (-3dB) is equivalent to losing one-half the power.

## Slide 56
Example 3.27
As the result shows +ve sign, so amplification (gain) of power = 10 dB.

## Slide 57: Signal to Noise Ratio (SNR or S/N)
Signal to noise ratio shows the ratio of signal power to noise power
Power often expressed in watts
S/N = signal power/noise power
Just a simple ratio

## Slide 58: Signal to Noise RatiodB (SNRdB or S/NdB)
Signal to noise ratiodB shows the ratio of signal power to noise power in decibels
S/NdB = 10 log10 (signal power/noise power)
Example 1: Signal power = 1000 watts, noise power = 20 mw
Example 2: Signal power = 100 w, noise power = 0.000002w

## Slide 59: Signal to Noise RatiodB
What if you know the S/Ndb but want to know the signal power level?
For example, you are given that S/Ndb = 85. What is the signal power level?

## Slide 60
One reason that engineers use the decibel to measure the changes in the strength of a signal is that decibel numbers can be added (or subtracted) when we are measuring several points (cascading) instead of just two. In Figure 3.27 a signal travels from point 1 to point 4. In this case, the decibel value can be calculated as
Example 3.28

## Slide 61
Figure 3.27 Decibels for Example 3.28

## Slide 62
Sometimes the decibel is used to measure signal power in milliwatts. In this case, it is referred to as dBm and is calculated as dBm = 10 log10 Pm , where Pm is the power in milliwatts. Calculate the power of a signal with dBm = −30.
Solution
We can calculate the power in the signal as
Example 3.29

## Slide 63
The loss in a cable is usually defined in decibels per kilometer (dB/km). If the signal at the beginning of a cable with −0.3 dB/km has a power of 2 mW, what is the power of the signal at 5 km?
Solution
The loss in the cable in decibels is 5 × (−0.3) = −1.5 dB. We can calculate the power as
Example 3.30

## Slide 64
Figure 3.28 Distortion (the second impairment)

## Slide 65: Distortion (Continued)
Distortion:
Distortion means that the signal changes its shape or form.
It can occur in composite signal made of different frequencies.
Each frequency has its own propagation speed through a medium and therefore its own delay in arriving at the final destination.
Delay changes the phase, therefore signals are distorted.

## Slide 66
Figure 3.29 Noise (the third impairment)

## Slide 67: Noise (Continued)
It is another cause of impairment.
Several types of noise such as thermal noise, induced noise, crosstalk noise, impulse noise may corrupt the signal.

## Slide 68
White Noise:
It is also called thermal noise or Gaussian noise. It is a continuous type of noise. It is always present to some degree and it dependent on the temperature of the medium. As temperature increases, level of noise increases. It can be significantly reduced but never be eliminated. It can be removed if signal passes through a regenerator before noise overwhelms original signal or passing the noisy signal through filters.
Impulse Noise:
It is a non-continuous noise and occur randomly. The noise is analog burst of energy. It can interfere both with analog and digital signals and often the original signal can’t be removed.
Types of Noise

## Slide 69
Crosstalk:
It is unwanted coupling between two different signal paths. This coupling can be electrical or electromagnetic. High humidity and wet weather increases the possibility of crosstalk..
Echo:
It is reflective feedback of transmitted signal as the signal moves through a medium. This occurs most often at junctions where wires are connected or at open end.
Types of Noise (Continued)

## Slide 70
The power of a signal is 10 mW and the power of the noise is 1 μW; what are the values of SNR and SNRdB ?
Solution
The values of SNR and SNRdB can be calculated as follows:
Example 3.31

## Slide 71
The values of SNR and SNRdB for a noiseless channel are
Example 3.32
We can never achieve this ratio in real life; it is an ideal.

## Slide 72
Figure 3.30 Two cases of SNR: a high SNR and a low SNR

## Slide 73
3-5 DATA RATE LIMITS
A very important consideration in data communications is how fast we can send data, in bits per second, over a channel. Data rate depends on three factors:
1. The bandwidth available
2. The level of the signals we use
3. The quality of the channel (the level of noise)
Noiseless Channel: Nyquist Bit Rate Noisy Channel: Shannon Capacity Using Both Limits
Topics discussed in this section:

## Slide 74
Increasing the levels of a signal may reduce the reliability of the system.
Note

## Slide 75: Channel Capacity
Data rate
  In bits per second
  Rate at which data can be communicated
Bandwidth
  In cycles per second of Hertz
  Constrained by transmitter and medium
Baud rate
  Frequency with which the components change

## Slide 76: BPS vs. Baud
Data rate rarely the same as baud rate
Examples:
TDC 361

## Slide 77: Channel Capacity
Nyquist
  Maximum data rate of a noiseless channel =
  2 * F * log2(L) bps
  Where F = frequency
  L = the number of discrete levels
  Example: F = 4000 Hz, L = 2

## Slide 78
Consider a noiseless channel with a bandwidth of 3000 Hz transmitting a signal with two signal levels. The maximum bit rate can be calculated as
Example 3.34

## Slide 79
Consider the same noiseless channel transmitting a signal with four signal levels (for each level, we send 2 bits). The maximum bit rate can be calculated as
Example 3.35

## Slide 80
We need to send 265 kbps over a noiseless channel with a bandwidth of 20 kHz. How many signal levels do we need?
Solution
We can use the Nyquist formula as shown:
Example 3.36
Since this result is not a power of 2, we need to either increase the number of levels or reduce the bit rate. If we have 128 levels, the bit rate is 280 kbps. If we have 64 levels, the bit rate is 240 kbps.

## Slide 81: Channel Capacity
Shannon (which includes noise)
  Maximum data rate (in bps) = B x log2(1 + S/N)
  B = bandwidth, or frequency
  S = signal power in watts
  N = noise power in watts (S/N = SNR)
  Example: B = 3400 Hz, S = 0.2 w, N = 0.0002 w
  Max data rate = 3400 x log2(1 + 1000)
  = 3400 x 9.97
  = 33898 bps

## Slide 82
Consider an extremely noisy channel in which the value of the signal-to-noise ratio is almost zero. In other words, the noise is so strong that the signal is faint. For this channel the capacity C is calculated as
Example 3.37
This means that the capacity of this channel is zero regardless of the bandwidth. In other words, we cannot receive any data through this channel.

## Slide 83
We can calculate the theoretical highest bit rate of a regular telephone line. A telephone line normally has a bandwidth of 3000. The signal-to-noise ratio is usually 3162. For this channel the capacity is calculated as
Example 3.38
This means that the highest bit rate for a telephone line is 34.860 kbps. If we want to send data faster than this, we can either increase the bandwidth of the line or improve the signal-to-noise ratio.

## Slide 84
The signal-to-noise ratio is often given in decibels. Assume that SNRdB = 36 and the channel bandwidth is 2 MHz. The theoretical channel capacity can be calculated as
Example 3.39

## Slide 85
We have a channel with a 1-MHz bandwidth. The SNR for this channel is 63. What are the appropriate bit rate and signal level?
Solution
First, we use the Shannon formula to find the upper limit.
Example 3.41

## Slide 86
The Shannon formula gives us 6 Mbps, the upper limit. For better performance we choose something lower, 4 Mbps, for example. Then we use the Nyquist formula to find the number of signal levels.
Example 3.41 (continued)

## Slide 87
The Shannon capacity gives us the upper limit; the Nyquist formula tells us how many signal levels we need.
Note

## Slide 88
In networking, we use the term bandwidth in two contexts.
❏ The first, bandwidth in hertz, refers to the range of frequencies in a composite signal or the range of frequencies that a channel can pass.
❏ The second, bandwidth in bits per second, refers to the speed of bit transmission in a channel or link.
Note

## Slide 89
As the bandwidth increases, so too can the data rate.
Stated another way, to transmit a high data rate, we need a wide bandwidth.
OR
We need to use a signaling technique that has a high number of signal levels.
The bandwidth of a subscriber line is 4 kHz for voice or data. The bandwidth of this line for data transmission
can be up to 56,000 bps using a sophisticated modem to change the digital signal to analog.
Example 3.42

## Slide 90
If the telephone company improves the quality of the line and increases the bandwidth to 8 kHz, we can send 112,000 bps by using the same technology as mentioned in Example 3.42.
Example 3.43

## Slide 91
Throughput:
When used in the context of communication networks, such as Ethernet or packet radio, throughput or network throughput is the rate of successful message delivery over a communication channel.
Throughput is usually measured in bits per second (bit/s or bps), and sometimes in data packets per second (p/s or pps) or data packets per time slot.
Jitter
Jitter, in networking, refers to small intermittent delays during data transfers. It can be caused by a number of factors including network congestion, collisions, and signal interference. Technically, jitter is the variation in latency — the delay between when a signal is transmitted and when it is received. All networks experience some amount of latency,
It is a problem if different packets of data encounter different delays and the application using the data at the receiver site is time sensitive.
Performance

## Slide 92
Bandwidth
Bandwidth describes the maximum data transfer rate of a network or Internet connection. It measures how much data can be sent over a specific connection in a given amount of time. For example, a gigabit Ethernet connection has a bandwidth of 1,000 Mbps (125 megabytes per second). An Internet connection via cable modem may provide 25 Mbps of bandwidth.
While bandwidth is used to describe network speeds, it does not measure how fast bits of data move from one location to another. Since data packets travel over electronic or fiber optic cables, the speed of each bit transferred is negligible. Instead, bandwidth measures how much data can flow through a specific connection at one time.
Performance(continued)

## Slide 93
Latency:
  Latency= propagation time + transmission time + queuing time + processing delay
Processing Time:
Propagation time= Distance/ (Propagation speed)
Transmission Time:
Propagation time= (Message Size)/ Bandwidth.
Queuing Time:
The time needed for each intermediate or end device to hold the message before it can be processed. It depends on the load imposed on the network.
Performance(continued)

## Slide 94
Performance(continued)
Processing Delay:
Processing delay is the time it takes router to process the packet header.
Transmission Time:
Propagation time= (Message Size)/ Bandwidth.
Queuing Time:
The time needed for each intermediate or end device to hold the message before it can be processed. It depends on the load imposed on the network.
Processing Delay:
Processing delay is the time it takes router to process the packet header.

## Slide 95: Review Questions
What is a composite signal?
How do you calculate a dB?
How do you calculate signal to noise ratio?
How do you read/create a frequency domain representation?
What is a dc component?

## Slide 96: Review Questions
How do you use the Nyquist formula?
  4000 Hz, 8 signal levels, data rate?
  50,000 bps data rate, 4000 Hz, how many signal levels?
How do you use the Shannon formula?
  8000 Hz, signal power = 20w, noise power = 0.002w, what is the data rate?
  5000 Hz, signal power = 50w, data rate = 20000bps, what is the possible noise power?